## Slide 1: Building-Integrated Thermal Energy Systems (BITES)
Professors: Jean Duquette
Kristen Schell
Ian Beausoleil-Morrison
Industry Partner: Chris Weissflog

## Slide 2
Canada is the fifth largest energy producer in the world and the eighth largest consumer of energy
Buildings account for 28% of secondary energy use in Canada and represent a large source of GHGs
Approximately 80% of residential use is attributed to space heating and hot water demands
Current strategies to reduce building loads typically consider heating, cooling and hot water needs separately
Hydro
Nuclear
Coal
Non-hydro renewables
Natural gas and oil
Chart: 
| Nuclear | Hydro | Coal | Natural gas and oil | Non-hydro renewables
 | 15 | 59 | 9 | 10 | 7
Canada’s Energy Mix
Chart: 
| Nuclear | Hydro | Coal | Natural gas and oil | Non-hydro renewables
 | 58.5 | 23.3 | 8.2 | 9.5

## Slide 3
Overall project focus is on an integrated approach for heating, cooling, ventilation, dehumidification, and domestic hot water heating for high efficiency low-rise multi-unit residential buildings (MURBs)
Design and optimization is required, including:
  Passive solar architecture
  High-performance envelope
  Multi-function heat pumps
  Heat recovery
  Geothermal storage
  Control strategies
Goal is to design a building integrated thermal energy system (BITES) that is replicable and delivers net-zero-energy-ready levels of performance

## Slide 4
Year 1 (2018-19): Simplified full-system design and analysis
  Analyze performance of BITES prototype (single-family residential scale) and identify opportunities for improving design
  Size key components (heat pumps, thermal storage, hydronic floor, geothermal field, thermal mass, windows) using simplified models for low-rise MURB

## Slide 5
Year 2 (2019-20): In-depth heat pump design and analysis
  Design, develop and analyze new heat pump cycles for use in heating, cooling and domestic hot water applications
  Develop heat transfer models of heat pump cycles in EES software
  Evaluate system feasibility based on seasonal performance, energy and exergetic efficiencies, system economics, environmental analysis, safety, noise, originality, esthetic of design, practicality, etc.
  Provide overall justification of design and performance, including assumptions and strategies

## Slide 6
Year 3 (2020-21): In-depth effluent heat recovery and geo-exchange design and analysis
  Investigate effluent waste heat recovery system types, layouts, and control strategies
  Investigate geo-exchange system types, layouts, and control strategies
  Develop simulation models to assess techno-economic performance of components and overall system

## Slide 7
Year 4 (2021-22): Detailed system design and numerical model development
  Design optimization of dehumidification/ventilation system (Year 1 design work used as basis)
  Design optimization of state-of-the-art multi-function transcritical CO2 heat pump (Year 2 design work used as basis)
  Design optimization of effluent heat recovery and geo-exchange systems (Year 3 design work used as basis)
  Detailed integrated system modeling and simulation using TRNSYS software (student training opportunities available)

## Slide 8
Thank you for your interest in BITES!
For more information, contact: Jean.Duquette@Carleton.ca